## Slide 1
01
DUET / AIRA
Humanising Voice AI
A month of building, breaking and measuring a real-time voice agent.
Duet repository experiments, August 2026
Notes: Start with the human experience, not the architecture. Ask: can an AI sales agent actually listen? We tried to build an empathetic ASBL Broadway sales concierge that could understand an Indian caller, answer from verified facts, take actions, and stop when interrupted. The important artifact is not a perfect bot. It is the evidence about what makes voice systems feel human—and what makes them fail.
SOURCES
- Duet repository experiments, August 2026
- Full source notes: docs/talk/FINAL_DECK_2026-08-25.md

## Slide 2
02
DUET · AIRA
A voice agent is a real-time control system
ONE SHARED STATE
conversation state
who owns the floor · current intent · cancellation version
01
Listen
capture speech
and ownership
02
Decide
facts · policy
and planning
03
Speak
stream voice
and stay cancellable
→
→
CONTINUOUS CAPABILITIES
They run beside the turn—not after it.
Remember
retain useful context
Yield
give the caller the floor
Act
request safe next steps
Duet architecture
Notes: A voice agent is not “an LLM with a microphone.” It is a timing-sensitive distributed system. It must continuously ingest audio, estimate who owns the floor, maintain state, retrieve facts, decide whether speech is safe, synthesize audio, and remain cancellable. Human-likeness is system behaviour, not a TTS voice setting.
SOURCES
- Duet architecture
- Full source notes: docs/talk/FINAL_DECK_2026-08-25.md

## Slide 3
03
DUET · AIRA
Demystifying the jargon
TERM
WHAT IT LITERALLY MEANS
IN A CONVERSATION
VAD
Voice Activity Detection
Is someone speaking?
ASR / STT
Automatic Speech Recognition / Speech-to-Text
What did they say?
EOU
End of Utterance / endpointing
Are they finished?
LLM TTFT
Large-language-model time to first token
When does thinking begin?
TTS TTFB
Text-to-speech time to first byte
When can speech begin?
Barge-in
Interruption detection and recovery
Can the caller take the floor?
RTF
Real-time factor
Can inference keep up with speech?
Duet learning guide
Notes: Clarify three easily confused latency clocks. ASR model processing is not the same as endpointing delay. LLM time-to-first-token is not total response completion. TTS time-to-first-byte is not total synthesis time. The listener experiences the composition plus transport and jitter buffering.
SOURCES
- Duet learning guide
- Full source notes: docs/talk/FINAL_DECK_2026-08-25.md

## Slide 4
04
DUET · AIRA
The waterfall tax
speech end
+
endpoint
+
ASR
+
reasoning
+
TTS
+
playback
wait + wait + wait + wait
Measured rich-response median: 2,715 ms
Decision 0021 · docs/LATENCY_ARCHITECTURE.md
Notes: In a naïve cascade, each stage waits for the previous stage to finish. Even respectable components produce an awkward pause when their tails add. In Duet’s first rich-response measurement the median was 2,715 ms: roughly 623 ms turn assembly, 1,739 ms complete reasoning, and 443 ms TTS first audio. That failed our own latency gate.
SOURCES
- Decision 0021 · docs/LATENCY_ARCHITECTURE.md
- Full source notes: docs/talk/FINAL_DECK_2026-08-25.md

## Slide 5
05
DUET · AIRA
Fast models do not guarantee a fast conversation
01
turn timing
02
reasoning
03
speech start
04
playout
wait for enough
silence to hand off
wait for stable intent
and verified facts
wait for a safe
first clause
wait for transport
and device buffer
FAST MODELS LOSE AT THE HANDOFF
Each component can be fast in isolation. The conversation waits until the next decision is safe to commit.
caller finished
→
meaning stable
→
safe first clause
→
playable audio
The delay is in the boundary between engines—not only inside the engine.
Duet latency architecture
Notes: Optimize the user-perceived interval: end of caller intent to audible first agent audio. Measure p50 and p95. Then pair latency with wrong-start rate, takeover rate, factuality and task success. A fast answer that starts before the user finishes is not low latency; it is an interruption defect.
SOURCES
- Duet latency architecture
- Full source notes: docs/talk/FINAL_DECK_2026-08-25.md

## Slide 6
06
DUET · AIRA
Duet’s thesis: guarded speculative duplex
partial transcript
quarantined
speculation
final meaning
confirmed
Start safe work early.
Commit only when meaning is stable.
Cancel everything stale.
Duet architecture; concurrency is prior art
Notes: Duet is not a new monolithic foundation model. It is a modular asynchronous architecture. Stable partial transcripts may start retrieval and reasoning. Results remain quarantined until the final transcript preserves meaning. Deterministic policy can pre-empt generation. Every generation and audio buffer carries cancellation state. This is our candidate engineering contribution; concurrency itself is prior art.
SOURCES
- Duet architecture; concurrency is prior art
- Full source notes: docs/talk/FINAL_DECK_2026-08-25.md

## Slide 7
07
DUET · AIRA
Concurrent lanes, causal gates
LISTEN
continuous audio
TURN
partial → stable → final
POLICY
consent · opt-out · barge-in · claims
PLAN
retrieval · reasoning
ACT
tool request
SPEAK
safe clause → audio
Duet runtime lanes
Notes: The lanes run concurrently, but information dependencies still exist. We need enough stable intent before selecting an answer, and enough verified content before speech. The architecture removes unnecessary waiting without pretending causality disappears. ASR remains armed while TTS plays so interruption can cancel speech immediately and create a new conversational state.
SOURCES
- Duet runtime lanes
- Full source notes: docs/talk/FINAL_DECK_2026-08-25.md

## Slide 8
08
DUET · AIRA
What runs inside Aira
Browser
Saaras
Duet
Gemini
Bulbul
Speaker
policy
facts
actions
telemetry
Duet Aira browser demo architecture
Notes: Browser audio is streamed continuously. Saaras v3 Realtime provides partial/final transcripts and speech events. Duet assembles turns, owns consent, barge-in, stale-response suppression and capability checks. Gemini Flash Lite plans grounded responses. An action adapter records or calls brochure, callback, CRM and site-visit tools. Bulbul v3 uses a pre-warmed persistent WebSocket. The local demo planner is a quota-independent fallback—not the production intelligence path.
SOURCES
- Duet Aira browser demo architecture
- Full source notes: docs/talk/FINAL_DECK_2026-08-25.md

## Slide 9
09
LIVE DEMO
DROP RECORDED DEMO HERE
disclosure · grounded answer · interruption · action · decision trace
Recorded Aira session
Notes: Insert the recorded Aira demo here. Show: disclosure and permission; one project question; one interruption; one brochure or site-visit action; the visible decision trace. Do not improvise with a live cloud model tomorrow. The recording path uses the local grounded demo planner so Gemini quota cannot break it.
SOURCES
- Recorded Aira session
- Full source notes: docs/talk/FINAL_DECK_2026-08-25.md

## Slide 10
10
DUET · AIRA
Speech quality is product quality
MEANING IN
If ASR misses the need, reasoning solves the wrong problem.
TRUST OUT
If TTS rushes the answer, correct reasoning still feels wrong.
Sarvam docs · Decisions 0009, 0017, 0020
Notes: Our first prototype sounded robotic because multiple defects compounded: a 16 kHz/24 kHz audio bug, synthetic voice artifacts, rushed pace, endpoint clipping, and a planner repeatedly pushing the same next step. Sarvam improved our real Indian-English captures and provides true streaming events, code-mix support, and a coherent Indian speech plane. It is not open weights; provider portability remains intentional.
SOURCES
- Sarvam docs · Decisions 0009, 0017, 0020
- Full source notes: docs/talk/FINAL_DECK_2026-08-25.md

## Slide 11
11
DUET · AIRA
The ASR eval changed the answer
WER at 5 dB noise ↓
base.en
14.1%
small.en
8.7%
MLX Whisper
3.4%
Parakeet
2.7%
In a noisy call, ASR choice determines what the agent believes before reasoning begins.
eval/asr/README.md · 30 utterances × 7 conditions
Notes: The first clean synthetic eval was too easy and could not discriminate. We added seeded noise, reverb, speed perturbation and clipping. The ranking then became clear and even reversed an earlier decision. Parakeet was also 0.04–0.08× real-time under contention, giving much more headroom. Limitation: synthetic Piper speech is still off-distribution; real microphone captures remain the acceptance set.
SOURCES
- eval/asr/README.md · 30 utterances × 7 conditions
- Full source notes: docs/talk/FINAL_DECK_2026-08-25.md

## Slide 12
12
DUET · AIRA
TTS: optimize the clock people hear
Time to first audio
0 ms
100 ms
200 ms
300 ms
400 ms
500 ms
Piper
83 ms
Sarvam warm
223 ms
Kokoro
380 ms
Fast speech start ≠ human voice quality
eval/tts/README.md · Decision 0022
Notes: Both engines synthesize faster than real time, so throughput was not the issue. TTFB lands directly on the critical path in a cascade. But speed alone is not quality: Piper was fast and sounded robotic. Human MOS/preference tests are required. Sarvam’s warm persistent TTS measured 223 ms first audio in our real path and sounded more appropriate for Indian-English conversation.
SOURCES
- eval/tts/README.md · Decision 0022
- Full source notes: docs/talk/FINAL_DECK_2026-08-25.md

## Slide 13
13
DUET · AIRA
Why Gemini won our reasoning gate
MEASURED ON OUR APPLE M5 · NOT A UNIVERSAL MODEL RANKING
Evidence level: 0 failed control · 1 relevant but ungated · 2 grounded sample · 3 132/136 checks
0
1
2
3
GROUNDING / POLICY
EVIDENCE
0 known failure
3 evaluated gate
0 ms
800 ms
1,600 ms
2,400 ms
3,200 ms
FIRST-PLAN LATENCY →
Qwen 0.8B
153 ms · fabricated facts
Gemma 1B
760–1,750 ms · schema/policy fails
Qwen 4B
1,623 ms · relevant, ungated
Gemma 4B
2,858–3,142 ms · grounded sample
Gemini Flash Lite
1,120 ms · 132/136 checks
Gemini was the only option that paired ~1.1 s planning with a gated grounded-response eval.
Gemini 3.1 Flash Lite docs · Decisions 0021–0022
Notes: Use precise language. Gemini 3.1 Flash Lite is designed for low-latency, high-frequency workflows and supports structured outputs and function calling. In our 17-scenario reasoning eval the richer path reached 97.1% checks. It remained the largest latency component and its free-tier quota broke a recording, so we added a deterministic fallback. The y-axis is deliberately an evidence scale—not a fabricated quality score: 0 means a known control failure, 1 relevant but not gated, 2 a grounded sample, and 3 the 17-scenario eval. “Best” here means among the models and policy traps we measured, not a universal frontier ranking.
SOURCES
- Gemini 3.1 Flash Lite docs · Decisions 0021–0022
- Full source notes: docs/talk/FINAL_DECK_2026-08-25.md

## Slide 14
14
DUET · AIRA
Local reasoning: the speed–reliability wall
MODEL
FIRST-PLAN LATENCY
OUTCOME
Qwen 0.8B
153 ms
fast, invented facts
Qwen 4B
1,623 ms
relevant, too slow
Gemma 1B
760–1,750 ms
schema / policy failures
Gemma 4B
2,858–3,142 ms
grounded sample, slower than Gemini
Gemini Flash Lite
1,120 ms
132/136 grounded-policy checks · chosen
Chosen: ~1.1 s planning + 132/136 grounded-policy checks.
Local model measurements · Decisions 0021–0022
Notes: Local is attractive for privacy, predictable cost and owned KV caching. But a smaller model that violates a financial-claim guard is not a viable sales brain. A larger local model that is slower than the API has no latency ROI on this laptop. Gemini was selected because it combined an observed 1,120 ms plan with 132/136 grounded-policy checks and structured tool support. Re-evaluate local candidates on production GPU hardware; do not generalize this Apple M5 result into “local models are bad.”
SOURCES
- Local model measurements · Decisions 0021–0022
- Full source notes: docs/talk/FINAL_DECK_2026-08-25.md

## Slide 15
15
DUET · AIRA
Moshi proved speed—and failed control
Handoff p50
Takeover
Overlap
Moshi duplex
240 ms
0.24
0.234
Cascade
1,880 ms
0.00
0.053
fast
polite
Moshi
In simple terms: it answered quickly, but often spoke at the wrong time.
Moshi paper · eval/bench/RESULTS.md
Notes: Moshi models caller and agent audio as parallel streams and has roughly 200 ms practical latency in its paper. On our 10-scenario benchmark it was eight times faster at the median and produced backchannels. It also grabbed the floor and rambled. Its p95 was 3.25 seconds. We benched it as the default product path because controllability and clarity mattered more than a median latency win.
SOURCES
- Moshi paper · eval/bench/RESULTS.md
- Full source notes: docs/talk/FINAL_DECK_2026-08-25.md

## Slide 16
16
DUET · AIRA
Experiment 1: earlier speculation did not prove speed
THE THESIS
Start reasoning after two stable words, rather than wait for four.
WHAT WE EXPECTED
The reply should begin meaningfully sooner.
BASELINE
1,943 ms
wait for four stable words
TWO-WORD SPECULATION
1,912 ms
start from two stable words
31 ms
31 ms difference across two live runs.
HONEST VERDICT
Too small and too few runs: noise, not a proven speedup.
GitHub PR #1 · Widen speculative-reasoning coverage
Notes: PR #1 lowered the stable-partial floor from four words to two while preserving opt-out, ambiguity and semantic-confirmation gates. The mechanism fired correctly, but n=2 live runs could not separate the 31 ms gap from normal variance. Gemini explicit cache storage was unavailable on the free tier, and implicit caching did not engage. We recorded the negative result rather than claiming a win.
SOURCES
- GitHub PR #1 · Widen speculative-reasoning coverage
- Full source notes: docs/talk/FINAL_DECK_2026-08-25.md

## Slide 17
17
DUET · AIRA
Experiment 2: the proxy win inverted
4.9× fewer free-run tokens
PROXY ✓
→
REALITY ✕
+59% takeovers
+41% overlap
8× worse handoff
In simple terms: we made the bot wait less; it interrupted people more often.
EVAL RULE · Eval the behaviour you care about—not the proxy that flatters your optimization.
GitHub PR #2 · docs/DUPLEX_STEERING.md
Notes: PR #2 used a local KV-cached brain and shortened Moshi’s quiet window. The first proxy looked spectacular. A real turn-taking A/B showed the “fast” configuration was ruder on every important metric. The quiet window was protective, not wasted latency. An even earlier 0.00-token result failed to reproduce due to state leakage in the harness. This is the talk’s key scientific lesson: eval the behaviour you care about, not the proxy that flatters your optimization.
SOURCES
- GitHub PR #2 · docs/DUPLEX_STEERING.md
- Full source notes: docs/talk/FINAL_DECK_2026-08-25.md

## Slide 18
18
DUET · AIRA
Evals are the new PRDs
scenario
metric
threshold
regression test
→
→
→
real call
Why: live calls reveal failures a prompt cannot. We made each one a repeatable test.
Duet CI and eval harnesses
Notes: We built deterministic unit tests, 17 grounded-reasoning scenarios, augmented ASR WER, TTS TTFB/RTF, turn-taking metrics, controlled barge-in smoke, container boot checks, and blind-human-eval protocols. Examples from real failures became tests: “I changed my mind,” “wait a minute,” clipped yes/no turns, duplicate actions, stale responses and opt-out. CI runs cheap deterministic gates on every commit; quota-consuming live evals run manually or on schedule.
SOURCES
- Duet CI and eval harnesses
- Full source notes: docs/talk/FINAL_DECK_2026-08-25.md

## Slide 19
19
DUET · AIRA
The model does not own trust
LLM
consent
opt-out
claims
staleness
capabilities
Deterministic code
Why: models can be wrong. They propose; deterministic code verifies consent, facts and permissions before speech or action.
Duet policy and action adapters
Notes: The LLM may propose an action. Only an action adapter may report accepted or completed. The same principle applies to brochure, callback, CRM and site visit. A “request” is not “done.” Opt-out cancels reasoning and speech immediately. Sensitive traits cannot drive lead scoring. Public product facts carry source IDs. The UI exposes an inspectable decision trace—intent, evidence, policy, facts—not private chain-of-thought.
SOURCES
- Duet policy and action adapters
- Full source notes: docs/talk/FINAL_DECK_2026-08-25.md

## Slide 20
20
DUET · AIRA
If you cannot replay it, you cannot improve it
TRACE ID
01
Langfuse
02
Prometheus + Grafana
03
Postgres
04
JSONL / Loki
Telemetry never blocks the audio path.
Duet observability stack
Notes: Telemetry is asynchronous and never blocks audio. Every session shares a trace ID across voice spans and the durable call record. Content is redacted by default. The latest four-minute demo produced 78 Langfuse observations, 11 user utterances, three playback cancellations and two accepted local actions.
SOURCES
- Duet observability stack
- Full source notes: docs/talk/FINAL_DECK_2026-08-25.md

## Slide 21
21
DUET · AIRA
Latest Aira run: fast, with one measurement bug
median response start
443 ms
interruptions
3
actions
2
user turns
11
cancel
cancel
cancel
action
action
p95 invalid — unmatched turn at session cutoff
Session 1787592808-61dd64 · trace 9722afa5…
Notes: This run used Sarvam ASR/TTS plus the local grounded planner, so reasoning cost and latency were zero. The 443 ms median is end-of-speech to first server audio, not browser-perceived latency. The stored p95 of 108.7 seconds is an instrumentation defect: one pending endpoint was matched to the session-limit closing speech. Show the defect. Fix the correlation before claiming a tail SLO.
SOURCES
- Session 1787592808-61dd64 · trace 9722afa5…
- Full source notes: docs/talk/FINAL_DECK_2026-08-25.md

## Slide 22
22
DUET · AIRA
Aira vs Sarvam Voice Agents: honest comparison
Aira local-plan
443 ms
measured · one session
Aira Gemini
1.62–2.90 s
measured · rich response
Sarvam
500 ms
vendor claim · definition unpublished
NOT YET APPLES-TO-APPLES
Duet traces · Sarvam Voice Agents product page
Notes: Sarvam now claims under 500 ms real-time latency and ₹3.50/min for its managed voice-agent stack. Their docs explicitly say there is no official round-trip SLA in the component guide. We cannot call this a benchmark yet. The fair test is identical scripts, network region, phone/WebRTC transport, 30+ calls, speech-end-to-audible-audio p50/p95, takeover, task success, factuality, human preference and cost.
SOURCES
- Duet traces · Sarvam Voice Agents product page
- Full source notes: docs/talk/FINAL_DECK_2026-08-25.md

## Slide 23
23
DUET · AIRA
Why India is a voice market
22
official languages
2M+
voice conversations/day¹
₹3.50
per minute¹
$6.3M
Bolna seed · 2026
Signals—not a top-down TAM proof.
¹Sarvam claims · Bolna funding announcement
Notes: India is voice-first, multilingual, code-mixed, mobile and operationally call-heavy. The moat is not only a pretty voice: noisy telephony, dialects, interruption, cost, compliance, integrations and reliability at large volumes. Sarvam reports more than two million voice conversations a day and is building a full-stack sovereign platform. Bolna raised $6.3M to make deployment self-serve. These are market signals, not a top-down TAM proof. Use in-house economics to validate the wedge.
SOURCES
- ¹Sarvam claims · Bolna funding announcement
- Full source notes: docs/talk/FINAL_DECK_2026-08-25.md

## Slide 24
24
DUET · AIRA
The wedge: remove junk work, not humans
AI
permission · intent · FAQs · qualification · follow-up
HUMAN ADVISOR
trust · nuance · negotiation · closure
Proposed ASBL pilot workflow
Notes: Start with ASBL inquiry reactivation and qualification. Aira can disclose itself, ask whether the caller wants a family home or investment, answer verified Broadway questions, collect timing and broad budget, and request a brochure, callback or site visit. Success is not calls automated. It is advisor hours saved, contact rate, qualified handoffs, factuality, opt-out compliance and incremental site visits.
SOURCES
- Proposed ASBL pilot workflow
- Full source notes: docs/talk/FINAL_DECK_2026-08-25.md

## Slide 25
25
DUET · AIRA
Prototype → production voice system
1
session isolation
2
telephony
3
DNC
4
human transfer
5
SLOs
6
load tests
7
replay
8
retention
9
incident response
The prototype is an instrument—not yet an outbound dialer.
Duet production-readiness audit
Notes: Commercial systems win through operational maturity: carrier integrations, regional routing, echo control, retries and circuit breakers, versioned prompts, campaign controls, abuse prevention, recordings and deletion, quality sampling, on-call alerts and graceful human handoff. The current app is single-session and browser-first. It is a strong instrument and demo, not yet an outbound production dialer.
SOURCES
- Duet production-readiness audit
- Full source notes: docs/talk/FINAL_DECK_2026-08-25.md

## Slide 26
26
DUET · AIRA
A 90-day proof, not a frontier-model lab
01
English · one project · one workflow
02
Shadow → internal → consented pilot
03
Promote only on measured gates
90 days
Duet 90-day pilot proposal
Notes: Week 1–3: instrument 100 historical, consent-safe scenarios and build the golden set. Week 4–6: connect real CRM actions and telephony in shadow mode. Week 7–9: small consented English pilot with human takeover. Week 10–12: compare agent versus current operation on qualification yield, complaints, factuality, latency, tool success and cost. Add Telugu/Hindi/code-mix only after separate speech and trust gates.
SOURCES
- Duet 90-day pilot proposal
- Full source notes: docs/talk/FINAL_DECK_2026-08-25.md

## Slide 27
27
DUET · AIRA
The lesson
Human is not a model.
Human is the behaviour of the whole system.
Duet experiment conclusion
Notes: We started by searching for a magical full-duplex model. We ended with a more useful view: natural conversation emerges from listening quality, timing, controllability, grounded reasoning, cancellable speech, trustworthy actions and a relentless evaluation loop. Buy the best current speech and reasoning primitives. Own the interaction state and evidence. Keep the research lane alive, but let production earn every claim.
SOURCES
- Duet experiment conclusion
- Full source notes: docs/talk/FINAL_DECK_2026-08-25.md

## Slide 28
28
DUET · AIRA
Appendix · research map
Moshi
two-stream full-duplex speech
PersonaPlex
role + voice conditioning
FD-Bench
293 conversations · 1,200 interruptions
Turn-taking studies
noise + decoding bias
Duet
guarded speculation + actions
arXiv:2410.00037 · 2507.19040 · 2605.20356
Notes: Moshi established a native two-stream speech architecture. PersonaPlex added role and voice conditioning. FD-Bench and newer turn-taking studies provide reproducible interaction tests. Duet's proposed contribution is modular guarded speculation plus capability-backed actions; novelty remains unproven until human ablations.
SOURCES
- arXiv:2410.00037 · 2507.19040 · 2605.20356
- Full source notes: docs/talk/FINAL_DECK_2026-08-25.md

## Slide 29
29
DUET · AIRA
Appendix · metrics that matter
ASR
WER / CER · accent · SNR · code-mix
TURN
endpoint · takeover · overlap · barge-stop
REASON
factuality · policy · task · TTFT
TTS
TTFB · MOS · intelligibility · glitches
SYSTEM
E2E p50/p95 · errors · cost/min
BUSINESS
qualified handoff · advisor time · visits
Duet evaluation framework
Notes: A production voice eval is layered. Measure recognition by accent and noise, turn-taking by endpoint and overlap, reasoning by factuality and task success, speech by TTFB and preference, and the whole system by tail latency, cost and business outcomes.
SOURCES
- Duet evaluation framework
- Full source notes: docs/talk/FINAL_DECK_2026-08-25.md

## Slide 30
30
DUET · AIRA
Appendix · questions to expect
Is this truly full duplex?
Controlled duplex today; Moshi is the native research lane.
Why not one speech-to-speech model?
Control, actions and deterministic policy still win here.
Why not a 20B local LLM?
Re-test on production GPU against the same gates.
Can this call customers tomorrow?
No—telephony, DNC, isolation and transfer are P0.
What is defensible?
Interaction state, eval data, workflows and reliability.
Duet engineering Q&A
Notes: Use these answers to stay candid. Aira is controlled duplex, not a finished native speech model. It is a serious instrument and architecture prototype, not yet an outbound production dialer. The defensible asset is the interaction and evidence loop.
SOURCES
- Duet engineering Q&A
- Full source notes: docs/talk/FINAL_DECK_2026-08-25.md